Modifications of the interface to the HCMMS_V7_DLL.DLL in relation to the interface to the HCMMS_V6.DLL

Please note:

The order of the variables has changed in the interface of the HCMMS_V7_DLL-DLL !

Modifications of the format are with gray background.

HCMMS_V7_DLL.DLL					HCMMS_V6.DLL

Name			Format				Name		Format

C_mode		INTEGER*4			CMODE	INTEGER*4

Bor_dis		INTEGER*4			BORDIS	INTEGER*4

PD			DOUBLE PRECISION	PD		DOUBLE PRECISION

Distance		DOUBLE PRECISION	DIST		DOUBLE PRECISION

H_Datab_Tx		INTEGER*2			HTT		INTEGER*4

H_Datab_Rx		INTEGER*2			HRT		INTEGER*4

HCM_error		INTEGER*4			ERROR	INTEGER*4

Heff			REAL*4			H1		REAL*4

Dh			REAL*4			DH		REAL*4

Dh_corr		REAL*4			CDH		REAL*4

Power_to_Rx		REAL*4			PR		REAL*4

Free_space_FS	REAL*4			E0		REAL*4

Land_FS		REAL*4			EL		REAL*4

Sea_FS		REAL*4			ES		REAL*4

Tx_ant_corr		REAL*4			C1		REAL*4

Tx_ant_type_corr	REAL*4			C2		REAL*4

Dir_Tx_Rx		DOUBLE PRECISION	DIRRX		REAL*4

V_angle_Tx_Rx	DOUBLE PRECISION	ANGLEV	REAL*4

Tx_TCA		REAL*4			TX_CLA	REAL*4

Rx_TCA		REAL*4			RX_CLA	REAL*4

Tx_TCA_corr		REAL*4			TX_CAC	REAL*4

Rx_TCA_corr		REAL*4			RX_CAC	REAL*4

D_sea_calculated	DOUBLE PRECISION	DSEA_C	REAL*4

Rx_ant_corr		REAL*4			C1R		REAL*4

Rx_ant_type_corr	REAL*4			C2R		REAL*4

Delta_frequency	DOUBLE PRECISION	DF		REAL*4

Corr_delta_f		REAL*4			CDF		REAL*4

Calculated_FS	REAL*4			EC		REAL*4

Perm_FS		REAL*4			EP		REAL*4

CBR_D		REAL*4			MAXRA	REAL*4

ERP_ref_Tx		REAL*4			ERPRT	REAL*4

Prot_margin		REAL*4			PROTM	REAL*4

I_str			CHARACTER*432		INTSTR	CHARACTER*459

(not longer used)					OFFDEY	INTEGER*4

(not longer used)					HT		INTEGER*4

(not longer used)					AM		REAL*4

(not longer used)					AMS		REAL*4

(not longer used)					DAV		REAL*4

(not longer used)					DAH		REAL*4

(not longer used)					AV		REAL*4

(not longer used)					DAZI		REAL*4

(not longer used)					DELE		REAL*4

(not longer used)					CSR		REAL*4

(not longer used)					CSI		REAL*4

(not longer used)					EP0		REAL*4

HCMMS_V/7_DLL.DLL					HCMMS_V6.DLL

Name			Format				Name		Format

(now in Calculated_FS)				MAXFS	REAL*4

(now in Distance)					DISBOR	DOUBLE PRECISION

(now in Dir_Tx_Rx)					DIRBOR	DOUBLE PRECISION

Modifications of the string variable (I_str / INTSTR)

The first modification is in “Corr.Fact.Acc.freq.diff”, starting position = 175. All following positions are changed! After “Version number” everything has changed.

All HCM_error codes and all Info(i) values are new!

VERSION 7

Start position 	Stop position	Description			In-/ Output		Format

1		15	Tx co-ordinates		Input		009E223350N4422

16		30	Rx co-ordinates		Input		009E223350N4422

31		34	Height of Tx site		Input		9999 or four blanks

35		38	Height of Rx site		Input		9999 or four blanks

39		45	Tx hor. ant. Type		Input		000ND00

46		52	Tx vert. ant. type		Input		000ND00

53		57	Tx Azimuth			Input		999.9

58		62	Tx Elevation			Input		+99.9

63		66	Tx Antenna height		Input		9999

67		70	Rx Antenna Height		Input		9999

71		71	Tx Type of antenna		Input		‘E’ or ‘I’

72		77	Max. radiated power		Input		+999.9

78		89	Tx Frequency			Input		99999.99999M

90		90	Channel occupation		Input		‘0’ or ‘1’

91		91	Sea temperature		Input		‘C’ or ‘W’

92		96	Tx Service area		Input		99999

97		101	Rx Service area		Input		99999

102		106	Distance over sea		Input		99999 or 5 blanks

107		118	Rx Frequency			Input		99999.99999M

119		127	Rx Design. of emm.		Input		14k0.....

128		136	Tx Design. of emm.		Input		14k0.....

137		143	Rx hor. ant. Type		Input		000ND00

144		150	Rx vert. ant. Type		Input		000ND00

151		155	Rx Azimuth			Input		999.9

156		160	Rx Elevation			Input		+99.9

161		161	Rx Type of ant.		Input		‘E’ or ‘I’

162		165	Rx Antenna gain		Input		99.9

166		169	Depolarisation loss		Input		99.9

170		174	Perm. Field strength		Input		+99.9 or 5 blanks

175		178	Corr. fact. acc. freq. diff.	Input		99.9 or four blanks

179		181	County code to calcul. to	Input		XXX

182		184	County code of Tx		Input		XXX

185		187	Max. cross border range	Input		999 or 3 blanks

188		250	Path of terrain data		Input		C:\TOPO..... (63 C)

251		313	Path of borderline data	Input		C:\BORDER (63 C)

314		376	Path of morphological data	Input		C:\MORPHO (63C)

377		382	Version number		Output

383		402	Info values (field, 20 values)	Output		‘T’rue  or ‘F’alse

403		417	Tx co-ordinates calculated	Output		008E213651N2137

418		432	Rx co-ordinates calculated	Output		007E413672N4127

433		???	Debug directory (optional)	Input		e.g. ‘C:\Temp’

VERSION 6

Start position 	Stop position	Description			In-/ Output		Format

1		15	Tx co-ordinates		Input		009E223350N4422

16		30	Rx co-ordinates		Input		009E223350N4422

31		34	Height of Tx site		Input		9999 or four blanks

35		38	Height of Rx site		Input		9999 or four blanks

39		45	Tx hor. ant. Type		Input		000ND00

46		52	Tx vert. ant. type		Input		000ND00

53		57	Tx Azimuth			Input		999.9

58		62	Tx Elevation			Input		+99.9

63		66	Tx Antenna height		Input		9999

67		70	Rx Antenna Height		Input		9999

71		71	Tx Type of antenna		Input		‘E’ or ‘I’

72		77	Max. radiated power		Input		+999.9

78		89	Tx Frequency			Input		99999.99999M

90		90	Channel occupation		Input		‘0’ or ‘1’

91		91	Sea temperature		Input		‘C’ or ‘W’

92		96	Tx Service area		Input		99999

97		101	Rx Service area		Input		99999

102		106	Distance over sea		Input		99999 or 5 blanks

107		118	Rx Frequency			Input		99999.99999M

119		127	Rx Design. of emm.		Input		14k0.....

128		136	Tx Design. of emm.		Input		14k0.....

137		143	Rx hor. ant. Type		Input		000ND00

144		150	Rx vert. ant. Type		Input		000ND00

151		155	Rx Azimuth			Input		999.9

156		160	Rx Elevation			Input		+99.9

161		161	Rx Type of ant.		Input		‘E’ or ‘I’

162		165	Rx Antenna gain		Input		99.9

166		169	Depolarisation loss		Input		99.9

170		174	Perm. Field strength		Input		+99.9 or 5 blanks

175		176	Corr. fact. acc. freq. diff.	Input		99 or two blanks

177		179	County code to calcul. to	Input		XXX

180		182	County code of Tx		Input		XXX

183		185	Max. cross border range	Input		999 or 3 blanks

186		248	Path of terrain data		Input		C:\TOPO..... (63 C)

249		311	Path of borderline data	Input		C:\BORDER (63 C)

*	312		374	Path of morphological data	Input		C:\MORPHO (63 C)

375		380	Version number		Output

381		383	Land figure (ITU-R)		Output

384		386	Sea figure (ITU-R)		Output

387		401	Line co-ordinates		Output		009E223350N2233

*	402		416	Tx co-ordinates calculated	Output		008E213651N2137

*	417		431	Rx co-ordinates calculated	Output		007E413672N4127

432		451	INFO2 values (field x 20)	Output		‘T’rue  or ‘F’alse

452		456	INFO3 values (field x 5)	Output		‘T’rue  or ‘F’alse

457		457	INFOA2 (Tx ant. 999XX99)	Output		‘T’rue  or ‘F’alse

458		458	INFOA3 (Rx ant. 999XX99)	Output		‘T’rue  or ‘F’alse

459		459	Vienna calculation		Output		‘T’rue  or ‘F’alse

460		???	Debug directory (optional)	Input		e.g. ‘C:\Temp’